## Slide 1
FINAL YEAR PROJECT
AEGIS
Adaptive Edge-Intelligence Guardian and Safety System
A smart child-safety wearable with on-device stress detection, GPS geofencing and instant SMS alerts.
PRESENTED BY
Barira Sarfraz 222201042
Nabeeha Zahid 222201009
SUPERVISED BY
Dr. Altaf Hussain
DEPARTMENT & DATE
Dept. of Computer Science
KICSIT Campus

## Slide 2
OUTLINE
Agenda
Adaptive Edge-Intelligence Guardian and Safety System
02
01
Introduction & Background
The problem and why AEGIS exists
02
Objectives, Scope & Methodology
Goals and how we built it
03
Literature & Comparison
Prior work and where AEGIS stands
04
Solution & Requirements
Our system, functional & non-functional
05
System Design & Diagrams
Architecture, hardware, UML
06
Dataset, ML Model & Results
WESAD, Random Forest, accuracy
07
Testing & Mobile App
Test cases and the parent app
08
Contribution, Limitations & Conclusion
Team, future work, wrap-up

## Slide 3
03
INTRODUCTION
Introduction
& Background
SECTION 03
Adaptive Edge-Intelligence Guardian and Safety System
03
Every year, parents of young children face the same fear: a child who wanders off, panics in a crowd, or faces a medical scare cannot always say so in time.
The problem
Existing child trackers only report GPS location and depend on a constant internet connection. They cannot sense distress, they go silent where there is no signal, and they say nothing about how the child actually feels.
Our answer
AEGIS is a wearable band for children aged 4-12 that reads physiological signals in real time, detects stress or danger on the device itself, tracks location, and alerts parents over SMS - working even with no internet at all.

## Slide 4
04
GOALS
Objectives
& Scope
What AEGIS sets out to achieve, and the boundaries we set for this project.
SECTION 04
Adaptive Edge-Intelligence Guardian and Safety System
04
01
Sense distress, not just location
Read heart rate, SpO2, skin response and temperature on the wrist.
02
Decide on the edge
Run the stress model on the ESP32 so alerts work without the cloud.
03
Alert reliably anywhere
Send SMS over GSM so parents are reached even with no internet.
04
Keep every child personal
Calibrate a 7-day baseline so detection fits the individual child.
05
Stay private and free
Restrict data per parent and build only on free-tier services.

## Slide 5
05
APPROACH
Methodology
& Development
An incremental, hardware-independent build so progress never stalls on parts.
SECTION 05
Adaptive Edge-Intelligence Guardian and Safety System
05
01
Design first
Architecture, data model and UML defined before code.
02
App & backend in parallel
Flutter screens built with dummy data, then wired to Firebase.
03
Model offline
Random Forest trained and validated on the WESAD dataset.
04
Firmware as pure logic
Z-score, sliding-window and geofence written and unit-tested off-device.
05
Integrate & test
Bring hardware, model, app and alerts together for end-to-end testing.

## Slide 6
BACKGROUND
Literature Review
Adaptive Edge-Intelligence Guardian and Safety System
06
Wearable stress detection
The WESAD dataset (Schmidt et al., 2018) established wrist physiological signals - HR, EDA, temperature, motion - as reliable cues for stress versus calm states.
On-device / edge ML
Research on TinyML shows compact models such as Random Forests can run on microcontrollers, enabling decisions without a network round-trip.
Child-tracking devices
Commercial trackers focus on GPS and calling; studies note their dependence on connectivity and the absence of any physiological awareness.
Physiological signals
Galvanic skin response and heart-rate variability are well-documented markers of acute stress, motivating multi-sensor fusion over location alone.

## Slide 7
WHERE WE STAND
AEGIS vs Existing Wearables
Adaptive Edge-Intelligence Guardian and Safety System
07
Capability | AEGIS | GPS Tracker | Kids' Smartwatch
Live GPS location | Yes | Yes | Yes
Physiological / stress sensing | Yes | No | Limited
On-device (edge) decisions | On-device | Cloud | Cloud
Works with no internet | Offline | No | No
SMS alert fallback | Yes | No | Limited
Geofencing | Yes | Limited | Yes
Backend cost | Free | Paid | Paid

## Slide 8
THE SYSTEM
Our Solution
Adaptive Edge-Intelligence Guardian and Safety System
08
01 Wearable Band
ESP32 reads the sensors, runs the model, calibrates, and decides - the brain of the system.
02 Edge ML Model
A Random Forest trained on WESAD, flashed to the band, classifying stress entirely on-device.
03 Parent App
A Flutter app that visualises vitals, location, alerts and analytics - it never makes decisions.
04 Firebase Backend
Free-tier Firestore, Auth and Cloud Messaging for storage, sync and push.

## Slide 9
09
REQUIREMENTS
Functional
Requirements
SECTION 09
Adaptive Edge-Intelligence Guardian and Safety System
09
01
Accounts & Authentication
Firebase Auth login; multiple children.
02
Live Vitals Dashboard
Real-time HR, SpO2, GSR and temperature.
03
Location & Geofence Map
Live GPS and safe-zone on OpenStreetMap.
04
Safe-Zone Configuration
Set the geofence centre and radius.
05
Alert History
Stress, breach and SpO2 alerts, logged.
06
Push Notifications
Instant alerts via Firebase Cloud Messaging.
07
Health Analytics
7-day vitals trends and stress charts.
08
Calibration Tracking
7-day baseline before alerts activate.

## Slide 10
10
QUALITY
Non-Functional
Requirements
SECTION 10
Adaptive Edge-Intelligence Guardian and Safety System
10
Reliability
Alerts must fire even offline - SMS over GSM, cached then synced.
Security & Privacy
Firestore rules restrict each parent to their own children's data.
Performance
A 10-second monitoring cycle with real-time updates in the app.
Power Efficiency
Duty-cycled sensing to extend battery life on a small LiPo cell.
Usability
The 7-day calibration is communicated clearly to parents.
Affordability
Built entirely on free-tier services - zero paid APIs.

## Slide 11
STACK
Tools & Technologies
Adaptive Edge-Intelligence Guardian and Safety System
11
Wearable
ESP32 · MAX30102 · MPU6050 · GSR · DS18B20 · NEO-6M GPS · SIM800L GSM
Machine Learning
Python · scikit-learn · Random Forest · WESAD dataset
Mobile App
Flutter · Dart · Provider · fl_chart · flutter_map
Backend (free tier)
Firebase Auth · Cloud Firestore · Cloud Messaging
Maps & Comms
OpenStreetMap · WiFi · BLE · GSM/SMS
Tooling
GitHub · GitHub Actions CI · PlatformIO

## Slide 12
12
ARCHITECTURE
System
Architecture
SECTION 12
Adaptive Edge-Intelligence Guardian and Safety System
12

## Slide 13
13
DATA FLOW
System Workflow
& Data Flow
SECTION 13
13

## Slide 14
14
HARDWARE
Hardware Block
& Circuit
SECTION 14
14

## Slide 15
15
BEHAVIOUR
Use Case
Diagram
SECTION 15
15
+
DIAGRAM PLACEHOLDER

## Slide 16
16
SCENARIOS
Descriptive
Use Cases
SECTION 16
Adaptive Edge-Intelligence Guardian and Safety System
16
UC-01 Register & Add Child
Actor · Parent
A parent signs up, creates their account and adds a child profile with a paired device.
UC-02 Configure Safe Zone
Actor · Parent
From the map the parent sets a geofence centre and radius that the band will monitor.
UC-03 Receive Breach Alert
Actor · Wearable
On leaving the safe zone the band vibrates, sends an SMS and logs an alert the app shows.

## Slide 17
USE CASE 01
View Real-Time Vitals
Adaptive Edge-Intelligence Guardian and Safety System
16
Typical Course of Actions | 
Actor's Action | System Response
1. Parent logs into the app. | 1. System authenticates the credentials and grants access.
2. Parent selects the child profile. | 1. System retrieves the data for the selected child's band.
3. Parent opens the vitals dashboard. | 1. System fetches the latest HR, SpO2, temperature and stress. 2. Displays them on the dashboard in real time.

## Slide 18
USE CASE 01 (CONTINUED)
View Real-Time Vitals
Adaptive Edge-Intelligence Guardian and Safety System
17
Alternative Course of Actions | 
Actor's Action | Alternative System Response
1a. Parent opens the app while offline. | 1a. System displays the last cached reading from the band.
1b. Connectivity is restored. | 1b. System resumes the typical flow with live data.
Exception Flow | 
Actor's Action | Exception System Response
1c. Parent enters incorrect login credentials. | 1c. System prompts re-entry of credentials.
1d. Login fails three times. | 1d. System locks the account for five minutes.

## Slide 19
USE CASE 02
Monitor Heart Rate & SpO2
Adaptive Edge-Intelligence Guardian and Safety System
18
Typical Course of Actions | 
Actor's Action | System Response
1. MAX30102 reads pulse and oxygen data. | 1. ESP32 computes heart rate and SpO2 values.
2. ESP32 compares readings to baseline thresholds. | 1. System uploads the validated readings to the cloud.
3. Parent opens the app to check trends. | 1. App fetches and displays HR and SpO2 history.
Alternative Course of Actions | 
Actor's Action | Alternative System Response
1a. Sensor noise is detected during reading. | 1a. Band filters the signal with the onboard ML model, then resumes once clean.
Exception Flow | 
Actor's Action | Exception System Response
1c. MAX30102 fails to respond. | 1c. Band logs the sensor error and sends a fallback alert via GSM.

## Slide 20
USE CASE 03
Monitor Body Temperature
Adaptive Edge-Intelligence Guardian and Safety System
19
Typical Course of Actions | 
Actor's Action | System Response
1. MLX90614 reads the child's body temperature. | 1. ESP32 compares the value to the configured threshold.
2. Reading is within the normal range. | 1. System stores the reading in the cloud.
3. Parent views the temperature trend. | 1. App displays the latest and historical temperature data.
Alternative Course of Actions | 
Actor's Action | Alternative System Response
1a. Ambient interference affects the reading. | 1a. Band recalibrates the sensor and resumes with a corrected reading.
Exception Flow | 
Actor's Action | Exception System Response
1c. Reading is out of range (>50C or <20C). | 1c. System activates anomaly detection and triggers an alert.

## Slide 21
USE CASE 04
Monitor Stress Level (GSR)
Adaptive Edge-Intelligence Guardian and Safety System
20
Typical Course of Actions | 
Actor's Action | System Response
1. GSR sensor measures skin conductance. | 1. ESP32 runs the on-device ML model to infer stress.
2. Stress level is classified. | 1. System streams the classified data to the cloud.
3. Parent opens the app. | 1. App displays the current and historical stress trend.
Alternative Course of Actions | 
Actor's Action | Alternative System Response
1a. GSR signal is weak or unstable. | 1a. System applies the child's baseline, then resumes.
Exception Flow | 
Actor's Action | Exception System Response
1c. Stress remains persistently high. | 1c. System triggers an alert without waiting for cloud confirmation.

## Slide 22
USE CASE 05
View Live Location & History
Adaptive Edge-Intelligence Guardian and Safety System
21
Typical Course of Actions | 
Actor's Action | System Response
1. Parent opens the location tab. | 1. App requests the latest location from the cloud.
2. NEO-6M GPS provides coordinates. | 1. ESP32 checks the coordinates against the geofence.
3. Band reports the verified position. | 1. System uploads coordinates and updates the map view.
Alternative Course of Actions | 
Actor's Action | Alternative System Response
1a. GPS signal is weak or unavailable. | 1a. Band falls back to cell-tower location and resumes.
Exception Flow | 
Actor's Action | Exception System Response
1c. Location upload fails. | 1c. System stores data locally and retries once reconnected.

## Slide 23
17
DATA MODEL
Entity-Relationship
Diagram
SECTION 17
17

## Slide 24
18
BEHAVIOUR
Activity
Diagram
SECTION 18
18

## Slide 25
19
STRUCTURE
Class
Diagram
SECTION 19
19

## Slide 26
20
INTERACTION
Sequence
Diagram
SECTION 20
20

## Slide 27
21
LEARNING
Dataset &
ML Model
The model is trained offline, then flashed to the band to run on-device.
SECTION 21
Adaptive Edge-Intelligence Guardian and Safety System
21
Dataset
WESAD - 15 subjects, wrist physiological signals
Algorithm
Random Forest · 15 trees · max depth 8
Output
Binary: NORMAL or STRESS
Features
14 inputs - HR, HRV, RMSSD, EDA, temperature, motion
On-device
Exported to a C header and run on the ESP32

## Slide 28
PERFORMANCE
ML Model Results
22
97.96%
Training accuracy
96.03%
Cross-validation
± 1.24%
CV std. deviation
Per-class metrics
Precision, recall and F1 (per NORMAL / STRESS class) are produced by the model test script and will be inserted here from its classification report.

## Slide 29
VERIFICATION
Detailed Test Cases
Adaptive Edge-Intelligence Guardian and Safety System
23
ID | Test Case | Layer | Type
TC-APP-001 | Parent account registration | Mobile App | Manual
TC-APP-002 | Define and persist a safe zone | Mobile App | Manual
TC-APP-003 | Invalid login credential rejection | Mobile App | Manual
TC-FW-001 | Baseline Z-score normalization | Firmware | Unit
TC-FW-002 | Stress classification on feature vector | Firmware | Unit
TC-INT-001 | End-to-end geofence breach alert | Integration | Black Box
TC-INT-002 | Alert flag triggers FCM push | Integration | Black Box
TC-HW-002 | GSM SMS fallback delivery | Hardware | Manual

## Slide 30
VERIFICATION
Detailed Test Cases
Adaptive Edge-Intelligence Guardian and Safety System
28
ML-EVAL-01
Model Classification Accuracy
PASS
OBJECTIVE
Evaluate the RF classifier on WESAD.
INPUT
WESAD: 14 features, 15 subjects.
EXPECTED RESULT
Accuracy at or above 90%.
ACTUAL RESULT
97.96% train; 96.03% CV (+/-1.24%).
PASS CRITERIA
Accuracy >= 90%, stable across folds.
TC-FW-001
Baseline Z-Score Normalization
OBJECTIVE
Standardize a reading vs the baseline.
INPUT
reading=80, mean=70, std=5.
EXPECTED RESULT
Returns 2.0.
ACTUAL RESULT
Returns 2.0.
PASS CRITERIA
Z-score equals the computed value.
PASSED

## Slide 31
VERIFICATION
Detailed Test Cases
Adaptive Edge-Intelligence Guardian and Safety System
29
TC-FW-002
Stress Classification
OBJECTIVE
Confirm the RF returns the expected label.
INPUT
A STRESS vector, then a NORMAL vector.
EXPECTED RESULT
Returns STRESS, then NORMAL.
ACTUAL RESULT
Returns STRESS, then NORMAL.
PASS CRITERIA
Labels match training annotations.
TC-FW-003
7-Day Calibration Window
OBJECTIVE
Finish calibration only after 7 days.
INPUT
7 days of mock HR/EDA/temp readings.
EXPECTED RESULT
Classification enabled from day 8.
ACTUAL RESULT
Classification enabled from day 8.
PASS CRITERIA
Baseline finalized; gated to day 8.
PASSED
PASSED

## Slide 32
VERIFICATION
Detailed Test Cases
Adaptive Edge-Intelligence Guardian and Safety System
30
TC-HW-001
Heart Rate Accuracy vs Oximeter
OBJECTIVE
MAX30102 HR vs a clinical oximeter.
INPUT
10 paired samples over 5 minutes.
EXPECTED RESULT
Within +/- 5 bpm of reference.
ACTUAL RESULT
Within +/- 5 bpm of reference.
PASS CRITERIA
Mean abs. difference <= 5 bpm.
TC-HW-002
SMS Fallback When WiFi Down
OBJECTIVE
GSM SMS fallback when WiFi fails.
INPUT
Stress alert with WiFi disabled.
EXPECTED RESULT
SMS received within fallback window.
ACTUAL RESULT
SMS received within fallback window.
PASS CRITERIA
Logs 'SMS sent: OK'; SMS received.
PASSED
PASSED

## Slide 33
VERIFICATION
Detailed Test Cases
TC-APP-001
Parent Account Registration
PASSED
OBJECTIVE
Register a parent via Firebase Auth.
INPUT
Name, unique email, valid password.
EXPECTED RESULT
Account created; onboarding opens.
ACTUAL RESULT
Account created; session active; onboarding opens.
PASS CRITERIA
Account in Firebase Auth; navigates.
TC-APP-002
Define and Persist a Safe Zone
PASSED
OBJECTIVE
Draw a safe zone; check it persists.
INPUT
Zone name, radius.
EXPECTED RESULT
Zone reappears after restart.
ACTUAL RESULT
Zone persisted; reloads after restart.
PASS CRITERIA
Geofence saved in Firestore.

## Slide 34
VERIFICATION
Detailed Test Cases
TC-APP-003
Invalid Login Rejection
PASSED
OBJECTIVE
Reject wrong credentials clearly.
INPUT
Valid email, wrong password.
EXPECTED RESULT
Error shown; no navigation.
ACTUAL RESULT
Error shown; no session/token issued.
PASS CRITERIA
Stays on login; no token issued.
TC-INT-001
End-to-End Geofence Breach
PASSED
OBJECTIVE
Breach: firmware through to app push.
INPUT
Mock GPS outside the safe zone.
EXPECTED RESULT
Push arrives within sync interval.
ACTUAL RESULT
Breach detected; GEOFENCE alert raised.
PASS CRITERIA
Alert in Firestore; push delivered.

## Slide 35
VERIFICATION
Detailed Test Cases
TC-INT-002
Alert Flag Triggers FCM Push
PASSED
OBJECTIVE
Alert write triggers an FCM push.
INPUT
Vitals record with alert = true.
EXPECTED RESULT
Push received; sync unaffected.
ACTUAL RESULT
Alert doc written; push-ready; sync unaffected.
PASS CRITERIA
Delivery log shows dispatch.

## Slide 36
Mobile App Design
Adaptive Edge-Intelligence Guardian and Safety System
24
The parent app's real flow - from sign-in to live monitoring. Insert native captures into the frames.

## Slide 37
On Boarding
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 38
Home Screen
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 39
Map Screen
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 40
Alerts Screen
24

## Slide 41
Trends Screen
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 42
AI Chatbot
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 43
Chatbot Screen
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 44
Chatbot Screen
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 45
Hardware
Adaptive Edge-Intelligence Guardian and Safety System
24

## Slide 46
25
CREDITS
Team
Contribution
A shared build - refine the exact split to match your own division of work.
SECTION 25
Adaptive Edge-Intelligence Guardian and Safety System
25
Barira Sarfraz
222201042
Flutter app screens & UI
Firebase integration
App–backend data flow
Nabeeha Zahid
222201009
ML model & WESAD pipeline
Firmware logic & geofencing
Documentation & testing

## Slide 47
27
HONESTY
Limitations &
Future Work
SECTION 27
Adaptive Edge-Intelligence Guardian and Safety System
27
Where we are today
Hardware is at dev-kit prototype stage
The model classifies stress as binary only
Battery life is not yet measured
Where we are headed
Full sensor and band integration
BLE pairing and power optimization
More affect classes beyond stress
A real-world pilot with families

## Slide 49
29
CLOSING
Conclusion
SECTION 29
Adaptive Edge-Intelligence Guardian and Safety System
29
AEGIS reimagines child safety as more than a dot on a map. By sensing distress on the wrist, deciding on the device, and reaching parents even without internet, it turns a tracker into a true guardian.
Edge-first
Decisions happen on the band, not the cloud.
Always reachable
SMS over GSM means alerts arrive offline.
Personal & private
Per-child calibration, per-parent data.
Built for zero cost
A complete system on free-tier services.

## Slide 50
SOURCES
References
Adaptive Edge-Intelligence Guardian and Safety System
30
1
Schmidt, P. et al. (2018). Introducing WESAD, a Multimodal Dataset for Wearable Stress and Affect Detection. ACM ICMI.
2
Breiman, L. (2001). Random Forests. Machine Learning, 45(1), 5-32.
3
Pedregosa, F. et al. (2011). Scikit-learn: Machine Learning in Python. JMLR 12.
4
Flutter Documentation. Google. flutter.dev
5
Firebase Documentation (Authentication, Cloud Firestore, Cloud Messaging). Google. firebase.google.com
6
OpenStreetMap Contributors. openstreetmap.org
7
Espressif Systems. ESP32 Technical Reference Manual.
8
fl_chart & flutter_map - Flutter community packages. pub.dev

## Slide 51
Thank You
Questions & Discussion
AEGIS · Adaptive Edge-Intelligence Guardian and Safety System
Barira Sarfraz · Nabeeha Zahid | Supervisor: Dr. Altaf Hussain